| PEOPLE’S COMMITTEE OF BA RIA – VUNG TAU PROVINCE -------- | SOCIALIST REPUBLIC OF VIETNAM Independence - Freedom - Happiness --------------- |
| --- | --- |
| No.: 43/2011/QĐ-UBND | Ba Ria Vung Tau, August 23, 2011 |

DECISION

REGULATIONS ON ZONING FOR EXHAUST EMISSION AND WASTEWATER DISCHARGE ACCORDING TO NATIONAL TECHNICAL REGULATION ON ENVIRONMENT IN THE AREA OF BA RIA-VUNG TAU PROVINCE

THE PEOPLE’S COMMITTEE OF BA RIA-VUNG TAU PROVINCE

Pursuant to the Law on Organization of the People’s Councils and the People’s Committees dated November 26, 2003;

Pursuant to the Law on Promulgation of Legislative Document of the People’s Councils, People’s Committees dated December 03, 2004;

Pursuant to the Law on Environment Protection dated November 29, 2005;

Pursuant to the Circular No. 25/2009/TT-BTNMT dated November 16, 2009 of the Ministry of Natural Resources and Environment regulating National technical regulation on the environment;

Implementing the Resolution No. 06-NQ/TU dated June 23, 2008 of the provincial standing committee of the Communist Party on environment in the area of Ba Ria-Vung Tau Province;

Implementing the Resolution No. 07-NQ/TU dated June 26, 2008 of the provincial standing committee of the Communist Party on industrial development in the area of Ba Ria-Vung Tau Province;

At the request of director of the Service of Natural Resources and Environment in the Statement No. 1369/TTr-STNMT dated August 05, 2011 requesting the promulgation of regulations on zoning for exhaust emission and wastewater discharge according to National technical regulation on environment in the area of Ba Ria-Vung Tau Province;

HEREBY DECIDE:

Article 1. Enclosed herewith are the regulations on zoning for exhaust emission and wastewater discharge according to National technical regulation on environment in the area of Ba Ria-Vung Tau Province (including three chapters, six articles and six appendices); Map of industrial wastewater discharge zoning in the area of Ba Ria – Vung Tau Province; Map of industrial emission zoning in the area of Ba Ria – Vung Tau Province

Article 2. This decision takes effect after ten days since the signing date and replaces the Decision No. 3528/2005/QĐ-UBND dated October 03, 2005 of the provincial People’s committee promulgating regulations on wastewater discharge, water zones and exhaust emission zoning to apply Vietnam’s Standards on environment (TCVN 2000, 2001) in the area of Ba Ria – Vung Tau Province.

Article 3. Regulations on zoning for exhaust emission and wastewater discharge according to National technical regulation on environment in the area of Ba Ria – Vung Tau Province are revised, supplemented to meet socio-economic development process in the administrative division or changed when competent authorities promulgate decision on replacements, amendments and supplements to National technical regulation on environment

Article 4. Director of the Service of Natural Resources and Environment is assigned to organize the implementation of this Decision and make regular reports to the People's committee of the province In case any difficulty arises during the implementation of this Decision, the Service of Natural Resources and Environment shall preside over and cooperate with departments, agencies, People’s committees of districts, communes, cities and relevant units in providing advice and making submission to the People’s committee of the province for consideration, revision and supplements as appropriate.

Article 5. Chief officers, People’s committees of provinces; directors of the Services of Natural Resources and Environment, Construction, Agriculture and Rural Development, Culture – Sports and Tourism, and Health; heads of management boards of industrial zones; presidents of People’s committees of Ba Ria—Vung Tau District, Vung Tau City; heads of relevant units, organizations and individuals shall be responsible for executing this Decision./.

|  | PP THE PEOPLE’S COMMITTEE PP THE PRESIDENT DEPUTY PRESIDENT Tran Ngoc Thoi |
| --- | --- |

PROVISIONS

EXHAUST EMISSION AND WASTEWATER DISCHARGE ZONING ACCORDING TO NATIONAL TECHNICAL REGULATION ON ENVIRONMENT IN THE AREA OF BA RIA-VUNG TAU PROVINCE (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

Chapter I

GENERAL PROVISIONS

Article 1. Scope and regulated entities

- Regulations on zoning for exhaust emission and wastewater discharge in the area of Ba Ria-Vung Tau Province are promulgated in order to provide guidance on the application of Vietnam’s Standards QCVN 24:2009/BTNMT - National technical regulation on industrial wastewater for determining maximum permissible limits of pollution factors contained in industrial wastewater when being discharged to the receiving waters, and QCVN 19:2009/BTNMT - National technical regulation on industrial emission for dust and inorganic substances for determining maximum permissible limits of dust and inorganic substances into the environment;

- These regulations apply to organizations, individuals involved in activities of discharging industrial wastewater into receiving waters and exhaust containing dust and inorganic substances into the air environment in the area of Ba Ria – Vung Tau Province.

- As for wastewater and exhaust with peculiar characteristics by area and industry of a number of productions, trading and service activities with separate regulations, such regulations shall be applied in combination with this Decision.

Article 2. Interpretation of terms and symbols

In this Decision, some terms and symbols shall be construed as follows:

1. Source of discharge: production facilities, industrial zones...that generate wastewater or exhaust.

2. Q: Flow rate of rivers, streams, canals, ditches as receiving waters;

3. V: Volume of basins as receiving waters

4. P: Flow rate of exhaust

5. P: Flow rate of wastewater

6. C: Value of pollution factors as defined in QCVN 19:2009/BTNMT, QCVN 24:2009/BTNMT;

7. Cmax: Maximum permissible limits of pollution factors of industrial wastewater or maximum permissible concentration of dust and inorganic substances contained in industrial emission.

8. Kf: Coefficients according to flow rate of wastewater, where:

- Kf1 = 1.2 if F ≤ 50 m3/day night

- Kf2 = 1.1 if 50 < F ≤ 500 m3/day night

- Kf3 = 1.1 if 500 < F ≤ 5,000 m3/day night

- Kf4 = 0.9 if F > 5,000 m3/day night

- Kf (1,2,3,4): Value corresponding to one of the cases Kf1, Kf2, Kf3,Kf4

9. Kp: Coefficient according to flow of exhaust, where:

- Kf1 = 1.0 if P ≤ 20,000 m3/hour

- Kf2 = 0.9 if 20.000 < P ≤ 100,000 m3/hour

- Kf3 = 0.8 if P > 100,000 m3/hour

- Kp(1,2,3): Value corresponding to one of the cases Kp1, Kp2, Kp3

10. Kqs: Coefficient according to flow rate of rivers, streams, canals, ditches that receive wastewater, where:

- Kqs = 0.9 if Q ≤ 50 m3/s

- Kqs = 1.0 if 50 < Q ≤ 200 m3/s.

- Kqs = 1.1 if 200 < Q ≤ 1,000 m3/s.

- Kqs = 1.2 if Q > 1.000 m3/s

11. Kqh: Coefficient according to volume of wastewater receiving basin, where:

- Kqh = 0.6 if V ≤ 10x106 m3

- Kqh = 0.8 if 10x106 m3 < V ≤ 100x106 m3

- Kqh = 1.0 if V > 10x106 m3

12. Kv: Coefficient of region where production, processing, trading and service facilities are located, where:

- Region 1 (Specialized forests, ranked historical and cultural remains; distance between production, processing, trading and service facilities and borderline of these areas are less than two kilometers): Coefficient Kv = 0.6 is applied.

- Region 2 (Inner cities, urbans types II, III, IV; distance between production, processing, trading and service facilities and borderline of these areas are less than two kilometers): Coefficient Kv = 0.8 is applied.

- Region 3 (Industrial zones, urbans type V; suburban zones types II, III, IV that are at least two kilometers away from borderline of inner cities, urbans; distance between production, processing, trading and service facilities and borderline of these areas are less than two kilometers): Coefficient Kv = 1.0 is applied.

- Region 4 (Rural area): Kv = 1.2 is applied.

- Region 4 (Rural area): Coefficient Kv = 1.2 is applied.

Chapter II

REGULATIONS ON DISCHARGE OF WASTEWATER INTO RECEIVING WATERS WITHIN THE AREA OF BA RIA – VUNG TAU PROVINCE

Article 3. Regulations on discharge of wastewater into receiving waters as surface water

- Discharge of wastewater into the rivers such as Thi Vai river, Dinh river, Ray river, Bang Chua- Du Du river, other rivers, streams and ditches and into receiving waters as basins shall be detailed in the Appendix enclosed herewith.

- As for rivers, streams and lakes that are not zoned as above but have data about flow value or volume and purpose of using water source, QCVN 24:2009/BTNMT shall be applied corresponding to the provisions set out in the Circular No. 25/2009/TT-BTNMT dated November 16, 2009 of the Ministry of Natural Resources and Environment regulating National technical regulation on environment.  In case data about flow/volume of small rivers, streams, lakes are not available, coefficients Kqs=0.9 (corresponding to small rivers, streams) and Kqh = 0.6 (corresponding to small lakes) can be applied.

Article 4. Regulations on wastewater generated from coastal production, trading and service activities

- All the coastal areas of Ba Ria – Vung Tau Province to be zoned shall be used for the purposes of aquatic production and water sports and entertainment.

- Wastewater generated from coastal production, trading and service facilities must be collected, processed to meet National technical regulation on environment and discharged to the central collection and drainage system of the area or re-used for operation of the unit without direct discharge to the coastal zones of Ba Ria – Vung Tau province.

- As for facilities that operate before this Decision is promulgated, time limit for execution shall be at least 12 months since the effective date of this Decision.

Article 5. Regulations on industrial production and concentrated cattle-breeding activities at the upper course of water zones used as a supply of tap water

- Wastewater generated from activities of industrial production and concentrated cattle-breeding at the upper course of water zones used as a supply of tap water must be collected, processed to meet National technical regulation on environment as regulated and discharged to the lower course of water zones used for supply of tap water or re-used for facilities’ operations.

- As for facilities that operate before this Decision is promulgated, time limit for execution shall be at least 12 months since the effective date of this Decision.

Chapter 3

EMISSION ZONING IN THE ADMINISTRATION DIVISION OF BA RIA-VUNG TAU PROVINCE

Article 6. Regulations on application of coefficient of region Kv

1. Region 1: Apply coefficient of region Kv= 0.6 including:

- Sanctuaries of Binh Chau – Phuoc Buu, Con Dao National Garden and distances under two kilometers from these areas;

2. Region 2: Apply coefficient of region Kv= 0.8 including:

- Urbans type II: Entire area of Vung Tau City except Long Son Commune and distances under two kilometers from borderline of Vung Tau City;

- Urbans type III: Ba Ria Urban consists of Long Toan, Phuoc Trung, Phuoc Nguyen, Phuoc Hiep, Phuoc Hung, Kim Dinh, Long Huong, Long Tam wards and distances under two kilometers from borderline of Ba Ria Urban;

3. Region 3: Apply coefficient of region Kv= 1 including:

- Industrial zones, industrial complexes within Ba Ria – Vung Tau Province and distances under two kilometers from borderline of these industrial zones and complexes;

- Urbans type V: Phu My Town of Tan Thanh District, Ngai Gia Town of Chau Duc District; Phuoc Buu Town of Xuyen Moc Commune; Long Hai and Long Dien towns of Long Dien District, Dat Do and Phuoc Hai towns of Dat Do Commune and distances under two kilometers from borderline of these towns;

- Long Son Commune, suburban zones of Ba Ria Town: Hoa Long, Long Phuoc, Tan Hung communes and distances under two kilometers from these areas;

4. Region 4: Apply coefficient of region Kv= 1.2 including:

- All the remaining area of Ba Ria-Vung Tau Province

5. In case borderline of production, processing trading and service facilities is in between from two regions and over, coefficient of region Kv  is applied corresponding to coefficient of region 1, 2, 3, 4, 5 respectively.

APPENDIX 1:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO THI VAI RIVER (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) |
| --- | --- | --- | --- |
|  |  | Value column C | Coefficient Kqs |
| 1. Thi Vai River | Other than supply of tap water | B | 1 |
| 2. Cai Mep River | Other than supply of tap water | B | 1 |
| 3. Rivers, streams, canals, ditches from second level and over | 3. Rivers, streams, canals, ditches from second level and over | 3. Rivers, streams, canals, ditches from second level and over | 3. Rivers, streams, canals, ditches from second level and over |
| Rang Ditch | Other than supply of tap water | B | 0.9 |
| Tac Ca Trung | Other than supply of tap water | B | 0.9 |
| Rang Ditch | Other than supply of tap water | B | 0.9 |
| Thi Vai Stream | Other than supply of tap water | B | 0.9 |
| Nhum Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Loi Stream | Other than supply of tap water | B | 0.9 |
| Sao Stream | Other than supply of tap water | B | 0.9 |
| Ban Thach Ditch | Other than supply of tap water | B | 0.9 |
| Cham Ditch | Other than supply of tap water | B | 0.9 |
| Dong Ditch | Other than supply of tap water | B | 0.9 |
| Ong Trinh Ditch | Other than supply of tap water | B | 0.9 |
| Nga Ba Ditch | Other than supply of tap water | B | 0.9 |
| Nga Tu Ditch | Other than supply of tap water | B | 0.9 |
| Ngon Cung Ditch | Other than supply of tap water | B | 0.9 |
| Tac Ditch | Other than supply of tap water | B | 0.9 |

APPENDIX 2:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO DINH RIVER NETWORK (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) |
| --- | --- | --- | --- |
|  |  | Value column C | Coefficient Kqs |
| 1. Dinh River |  |  |  |
| From Dinh River dam (old pump station of Dinh River Water Supply Station) to upper course | Other than supply of tap water | B | 0.9 |
| From Dinh River dam down to lower course | Other than supply of tap water | B | 1 |
| 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels |
| Xoai River (upper course of Da Den Lake) | Supply of tap water | A (Apply Article 5) | 0.9 |
| Gia Hop Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Tra Rang Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Rock Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Com Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Chich Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Nhat Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Lup Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Ca River (lower course of Da Den Lake) | Other than supply of tap water | B | 0.9 |
| Soui Stream | Other than supply of tap water | B | 0.9 |
| Chau Pha Stream (from Chau Pha Lake to upper course) | Supply of tap water | A (Apply Article 5) | 0.9 |
| Chau Pha Stream (from Chau Pha Lake down to lower course) | Other than supply of tap water | B | 0.9 |
| Stone Stream | Other than supply of tap water | B | 0.9 |
| Giao Keo Stream | Other than supply of tap water | B | 0.9 |
| Hoa Nuoc Stream | Other than supply of tap water | B | 0.9 |
| Sand Stream | Other than supply of tap water | B | 0.9 |
| Lung Stream | Other than supply of tap water | B | 0.9 |
| Song Cau Stream | Other than supply of tap water | B | 0.9 |
| Ba Coi River | Other than supply of tap water | B | 1 |
| Cay Khe River | Other than supply of tap water | B | 0.9 |
| Sau Ditch | Other than supply of tap water | B | 0.9 |
| Cua Lap River | Other than supply of tap water | B | 1 |
| Co May River | Other than supply of tap water | B | 1 |
| Dung Dan River | Other than supply of tap water | B | 0.9 |

APPENDIX 3:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO RAY RIVER NETWORK (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) |
| --- | --- | --- | --- |
|  |  | Value column C | Coefficient Kqs |
| 1. Ray River |  |  |  |
| From Ray River dam (construction site of Ray River basin) to upper course | Supply of tap water | A (Apply Article 5) | 0.9 |
| From Ray River dam (construction site of Ray River basin) to lower course of Ray River – Loc An gate | Other than supply of tap water | B | 0.9 |
| 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels |
| Xa Ac Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Nung Tung Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Tam Bo River | Supply of tap water | A (Apply Article 5) | 0.9 |
| Gia Hoet Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Tam Bong Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Monkey Stream | Other than supply of tap water | B | 0.9 |
| Giau Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Giao Stream | Other than supply of tap water | B | 0.9 |
| Ta Lung Stream | Other than supply of tap water | B | 0.9 |
| Lo O Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Deep Stream | Other than supply of tap water | B | 0.9 |
| Bamboo Stream | Other than supply of tap water | B | 0.9 |
| Dang River | Other than supply of tap water | B | 0.9 |
| Say Stream | Other than supply of tap water | B | 0.9 |
| Ba La Stream | Other than supply of tap water | B | 0.9 |
| Ma Troc Stream | Other than supply of tap water | B | 0.9 |
| Sao River | Other than supply of tap water | B | 0.9 |
| Ba Dap River | Other than supply of tap water | B | 0.9 |
| Hoa River - from Hoa River dam (construction site of Hoa River basin (X 107025’41,88'; Y 10031’49,08’’) to upper course of Hoa River | Supply of tap water | A (Apply Article 5) | 0.9 |
| Hoa River - from Hoa River dam to lower course (confluence of Hoa River and Ray River) | Other than supply of tap water | B | 0.9 |
| Cay Gia Stream | Other than supply of tap water | B | 0.9 |
| Sand Stream 2 | Other than supply of tap water | B | 0.9 |
| Rock Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Le Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Dan Y Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Cau 3 Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Sand Stream | Other than supply of tap water | B | 0.9 |
| Bear Stream | Other than supply of tap water | B | 0.9 |
| Soc Stream | Other than supply of tap water | B | 0.9 |
| Don Stream | Other than supply of tap water | B | 0.9 |
| U Stream | Other than supply of tap water | B | 0.9 |

APPENDIX 4:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO BANG CHUA – DU DU RIVER NETWORK (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) |
| --- | --- | --- | --- |
|  |  | Value column C | Coefficient Kqs |
| 1. Bang Chua – Du Du River | Other than supply of tap water | B | 0.9 |
| 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels | 2. Rivers, streams, canals, ditches from 2nd - n levels |
| Bang Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Dam La Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Cau 5 Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Cau 6 Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Cac Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Rock Stream | Other than supply of tap water | B | 0.9 |
| Lu Hu Stream | Other than supply of tap water | B | 0.9 |
| Nho Stream | Other than supply of tap water | B | 0.9 |

APPENDIX 5:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO OTHER RIVERS, STREAMS AND DITCHES (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) |
| --- | --- | --- | --- |
|  |  | Value column C | Coefficient Kqs |
| 1. Rivers, streams along the sea | 1. Rivers, streams along the sea | 1. Rivers, streams along the sea | 1. Rivers, streams along the sea |
| Tac Lon River | Other than supply of tap water | B | 0.9 |
| Ong Ditch | Other than supply of tap water | B | 0.9 |
| Ho Bai Spring | Other than supply of tap water | B | 0.9 |
| Ong Ben Ditch | Other than supply of tap water | B | 0.9 |
| Ca Coc River | Other than supply of tap water | B | 0.9 |
| Mo Nhat River | Other than supply of tap water | B | 0.9 |
| Nhu Be Spring | Other than supply of tap water | B | 0.9 |
| Nhu Giua Spring | Other than supply of tap water | B | 0.9 |
| Nhu Dau Spring | Other than supply of tap water | B | 0.9 |
| Cong Doi Ditch | Other than supply of tap water | B | 0.9 |
| Ngot Stream | Other than supply of tap water | B | 0.9 |
| Tac Ditch | Other than supply of tap water | B | 0.9 |
| Ngon Cung Ditch | Other than supply of tap water | B | 0.9 |
| Gieng Muoi Ditch | Other than supply of tap water | B | 0.9 |
| Bamboo Ditch | Other than supply of tap water | B | 0.9 |
| Ba Sinh Stream | Other than supply of tap water | B | 0.9 |
| Lu Thuyen Spring | Other than supply of tap water | B | 0.9 |
| Tac So Dua | Other than supply of tap water | B | 0.9 |
| Tac Hao | Other than supply of tap water | B | 0.9 |
| Cha Va River | Other than supply of tap water | B | 0.9 |
| Rang River | Other than supply of tap water | B | 0.9 |
| Bai Bun River | Other than supply of tap water | B | 0.9 |
| Ngon Ong Men Ditch | Other than supply of tap water | B | 0.9 |
| Xom Moi River | Other than supply of tap water | B | 0.9 |
| Ong Bong River | Other than supply of tap water | B | 0.9 |
| Bo Hoc River | Other than supply of tap water | B | 0.9 |
| Mui Giui River | Other than supply of tap water | B | 0.9 |
| Ba Tim River | Other than supply of tap water | B | 0.9 |
| Lach Van River | Other than supply of tap water | B | 0.9 |
| Ben Go Ditch | Other than supply of tap water | B | 0.9 |
| Cung Ban Ditch | Other than supply of tap water | B | 0.9 |
| Lach Van River | Other than supply of tap water | B | 0.9 |
| Long Hoa River | Other than supply of tap water | B | 0.9 |
| Go Gang Ditch | Other than supply of tap water | B | 0.9 |
| Mui Giui Ditch | Other than supply of tap water | B | 0.9 |
| 2. Other rivers, streams | Other than supply of tap water | B | 0.9 |
| Da Bang Stream | Supply of tap water | A (Apply Article 5) | 0.9 |
| Ngang Stream | Other than supply of tap water | B | 0.9 |
| Ba San Stream | Other than supply of tap water | B | 0.9 |
| Mon Stream | Other than supply of tap water | B | 0.9 |

APPENDIX 6:

REGULATIONS ON DISCHARGE OF WASTEWATER INTO RECEIVING WATERS AS LAKES (Enclosed with the Decision No. 43/2011/QĐ-UBND dated August 23, 2011 of the People’s Committee of Ba Ria - Vung Tau Province)

| No. | Name | Use purpose | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Applied QCVN 24:2009/BTNMT Cmax = C.Kas.Kf(1,2,3,4) | Notes |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Value column C | Coefficient Kqs |  |
| 1 | But Thien Lake | Supply of tap water | B | 0.6 | Dat Do and Long Dien districts |
| 2 | Da Bang 1 Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Dat Do and Chau Duc districts |
| 3 | Da Bang 2 Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 4 | Lo O Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 5 | So Bong Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Dat Do District |
| 6 | Suoi Mon Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 7 | Gia Hoet Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Chau Duc District |
| 8 | Kim Long Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 9 | Tam Bo Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 10 | Suoi Lup Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 11 | Da Den Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 12 | Ray River Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 13 | Gia Hop 1 Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 14 | Gia Hop 2 Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 15 | Suoi Chich Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 16 | Suoi Giau Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 17 | Nui Nham Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 18 | Suoi Da Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Tan Thanh District |
| 19 | Chau Pha Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 20 | Phuoc Binh Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 21 | Nhum Stream Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 22 | Nha Be Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 23 | Giao Keo Lake | Other than supply of tap water | B | 0.6 |  |
| 24 | Suoi Giao Lake | Other than supply of tap water | B | 0.6 |  |
| 25 | Nuoc Ngot Lake | Other than supply of tap water | B | 0.6 |  |
| 26 | Rach Chanh Lake | Other than supply of tap water | B | 0.6 |  |
| 27 | Moc Xuyen Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Xuyen Moc District |
| 28 | Sand Stream Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 29 | Hoa River Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 30 | Binh Chau Lake | Other than supply of tap water | B | 0.6 |  |
| 31 | Kinh River Lake | Other than supply of tap water | B | 0.6 |  |
| 32 | Mang Ca Lake | Other than supply of tap water | B | 0.6 | Vung Tau City |
| 33 | Bau Trung Lake | Other than supply of tap water | B | 0.6 |  |
| 34 | Bau Sen Lake | Other than supply of tap water | B | 0.6 |  |
| 35 | Vo Thi Sau Lake | Other than supply of tap water | B | 0.6 |  |
| 36 | Quang Trung Lake | Supply of tap water | A (Apply Article 5) | 0.6 | Con Dao District |
| 37 | An Hai Lake | Supply of tap water | A (Apply Article 5) | 0.6 |  |
| 38 | Phi Van Lake | Other than supply of tap water | B | 0.6 |  |