| THE MINISTRY OF CONSTRUCTION ------- | SOCIALIST REPUBLIC OF VIETNAM Independence – Freedom - Happiness --------------- |
| --- | --- |
| No. 507/QĐ-BXD | Hanoi, April 27, 2015 |

DECISION

APPROVAL FOR LIME INDUSTRY DEVELOPMENT PLANNING TO 2020 AND A VISION TO 2030

THE MINISTER OF CONSTRUCTION

Pursuant to the Law on Construction No. 50/2014/QH13 dated June 18, 2014;

Pursuant to the Law on Mineral No. 60/2010/QH12 dated November 17, 2010;

Pursuant to the Decree No. 62/2013/NĐ-CP dated June 25, 2013 by the Government defining the functions, tasks, entitlements and organizational structure of the Ministry of Construction;

Pursuant to the Government’s Decree No. 15/2012/NĐ-CP dated March 09, 2012 detailing the implementation of a number of articles of the Law on Mineral;

Pursuant to the Government’s Decree No. 124/2007/NĐ-CP dated July 31, 2007 on management of building materials;

Pursuant to the Prime Minister’s Decision No. 1469/QĐ-TTg dated August 22, 2014 on approval for general building materials development planning in Vietnam to 2020 and a vision to 2030;

Pursuant to the Prime Minister’s Directive No. 03/CT-TTg dated March 30, 2015 reinforcing the exercise of policies and laws on mineral;

Pursuant to the Prime Minister’s empowerment at the Official Dispatch No. 284/VPCP-KTN  dated January 13, 2015 on approval for lime industry development planning in Vietnam to 2020 and a vision to 2030;

At the request of Director General of the Department of building materials;

HEREBY DECIDE

Article 1: Approve lime industry development planning in Vietnam to 2020 and a vision to 2030 as follows:

1. Viewpoints:

a) Develop production of lime products of high value, stability and sustainability on the basis of effective use of natural resources; use replacement raw materials in the direction of green technology and environmental protection;

b) Invest in the development of lime production facilities with state-of-the-art technology, high level of mechanization and automation to enhance product quality; diversify categories to meet demands of sectors, areas of industrial, agricultural production, construction and exportation; move toward removal of lime production facilities spontaneously and manually grown, causing environmental pollution and not in accordance with the planning;

c) Encourage economic sectors to take part in investment and production of lime with environmentally friendly state-of-the-art technology;

2. Targets:

a) Calculate demands for lime of each sector, area of industrial and agricultural production, construction and exportation; define projects, zones of raw materials for lime production projects, and construct an implementation itinerary to meet demand-supply balance in each stage;

b) Define appropriate scale and capacity, state-of-the-art technology and equipment saving raw materials, fuel and meeting environmental standards;

c) To 2016, remove at least 50% of discontinued manual kilns across the country; to 2020, removal all of discontinued and continued kilns across the country;

3. Lime industry development planning to 2020:

a) Forecasts about demand for lime:

| No. | Area of use | Forecasts about demand (1,000 ton) | Forecasts about demand (1,000 ton) |
| --- | --- | --- | --- |
|  |  | 2015 | 2020 |
| I | DEMANDS | 3,990 | 5,680 |
| 1 | Industry, construction | 1,360 | 2,370 |
| 1.1 | Cast iron refining industry | 920 | 1.440 |
| 1.2 | Steel refining industry | 120 | 170 |
| 1.3 | Aluminium industry | 320 | 760 |
| 1.4 | Exhaust treatment for thermo-power plants | 100 | 150 |
| 1.5 | Production of autoclaved aerated concrete AAC | 150 | 410 |
| 2 | Agricultural production |  |  |
| 2.1 | Chemical industry | 250 | 400 |
| 2.2 | Paper industry | 790 | 880 |
| 2.3 | Sugar cane industry | 80 | 100 |
| 2.4 | Improvement of alkaline soil | 600 | 600 |
| 2.5 | Aquaculture | 550 | 600 |
| 3 | Demands (3%) | 120 | 160 |
| II | EXPORTATION | 1,500 | 2,500 |
|  | Total | 5,490 | 8,180 |

b) Requirements for capacity scale and equipment technology:

- Capacity scale:

Only new lines with capacity ≥ 200 ton/day (60,000 ton/year) are considered for investment.

- Technology, equipment:

* Lime production facilities to be invested must go for environmentally friendly advanced technology with green technology, mechanization and automation being highly encouraged to meet some specific criteria as follows:

+ Loss of energy: < 900 kcal/kg;

+ Loss of electrical energy: < 30 kWh/ton;

+ Dust emission: < 30 mg/Nm3

* Use of alternatives to fossil fuel must be studied to save natural resources and reduce environmental pollution.

c) Planning for zones of raw materials:

+ Add 18 limestone quarries as prescribed in Appendix II enclosed with the Prime Minister’s Decision No. 45/QĐ-TTg dated January 09, 2012 approving the planning for survey, exploitation, processing and use of mineral as building materials in Vietnam to 2020 to the list of quarries of raw materials for lime production (Part 1, Appendix III enclosed herewith);

+ Revise and add some limestone quarries reserved for cement industries as prescribed the Prime Minister’s Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 to the list of quarries of raw materials for lime production (Part 2, Appendix III enclosed herewith);

+ Define quarries of raw materials for production facilities, investment projects as prescribed in the planning;

+ Issuance of permits for new investment projects must be closely associated with sources of limestone raw materials; capacity scale to be invested must be in conformity with permissible deposits.

d) Itinerary of implementation to 2015:

- Total design capacity in 2015 achieves approximately 5.8 million ton/year, specifically:

+ Mechanized kilns: 4.3 million ton/year;

+ Manual kilns (continued and discontinued): 1.5 million ton/year;

- Investment orientation:

+ Invest in technological innovation, improvement of product quality, reduction of loss of fuel to achieve standards of technology and environment at existing production facilities (Appendix I enclosed herewith);

+ Carry out 22 new investment projects with investors identified (Appendix I enclosed herewith) with total design capacity of 2.85 million ton/year and plan to carry out another four projects with investors unidentified (Appendix II enclosed herewith) with total design capacity of 350,000 ton/year;

+ No permission shall be issued to continued and discontinued manual kilns across the country;

+ Up to 2016, at least 50% of discontinued manual kilns across the country shall be removed and approximately 500,000 ton of lime products per year produced by discontinued manual kilns are maintained;

+ Maintain approximately 1 million ton of lime products per year produced by continued manual kilns;

dd) Itinerary of implementation from 2016 - 2020:

- Total design capacity in 2020 expected to achieve approximately 8.96 million ton/year

- Investment orientation:

+ Maintain and promote capacity of mechanized lime production facilities already invested to achieve approximately 4.3 million ton/year;

- Up to 2020, all discontinued manual kilns across the country shall be removed;

+ Invest in expansion of capacity of 17 projects with investors identified (Appendix I enclosed herewith) with total design capacity of 3.46 million ton/year and 17 projects with investors unidentified (Appendix II enclosed herewith) with total design capacity of 1.2 million ton/year;

4. A vision for lime industry development to 2030:

- Demand for lime in 2030 is expected to reach from nine to ten million ton, of which:

+ Domestic consumption: Seven million ton

+ Exportation: Three ton

Investment in production development must be carried out to meet approximately 10 million ton of lime product in demand as expected in 2030;

Article 2. Implementation

1. The Ministry of Construction

Organize announcement and dissemination of the lime industry development planning to 2020 and a vision to 2030 as prescribed to localities, sectors, levels and businesses for understanding and execution;

Instruct localities to carry out management of lime production according to the planning; supervise and inspect the implementation of the content of the planning; impose strict punishments for violations;

Provide advice on investment projects of lime production based on the orientation of lime production investment and development to ensure the implementation is in compliance with the planning;

Carry out the checks on the implementation of the planning annually; make revisions to the list of projects, investors and zones of lime raw materials based on specific conditions;

Preside over and cooperate with the Ministry of Science and Technology in providing guidance and conducting research to build and promulgate National technical regulations, national standards on industrial lime to suit the Law on Technical regulations and standards;

Carry out regular inspection and monitoring of exploitation and processing of limestone mineral to ensure sources of raw materials for lime production; reinforce management to ensure balance of supply and demand for domestic use and exportation of lime;

2. The Ministry of Natural Resources and Environment

Preside over and cooperate with relevant agencies in organizing survey and research for additional sources of lime raw materials; continue to carry out survey and research to add more limestone quarries that satisfy requirements for supply of sources of raw materials for lime production;

Preside over and cooperate with relevant agencies in conducting the inspection of environmental criteria in lime production and quarry exploitation to minimize negative effects on landscape and environment;

Provide guidance to quarry exploitation units on application and compliance with advanced exploitation technology saving natural resources, ensuring safety, environmental protection and landscape;

3. The Ministry of Industry and Trade

Preside over designing and manufacturing equipment, spare parts for mechanized lime production lines;

Conduct research and promulgate policies supporting trade promotion and creating conditions for businesses to carry out exportation of lime with high outcomes.

4. The Ministry of Science and Technology:

Organize activities of science and technology in lime production development, introduce and disseminate state-of-the-art technologies in the world;

Conduct the assessment of technical regulations and standards on lime production and make announcement of national standards as prescribed;

5. People’s committees of central-affiliated cities and provinces:

Organize the implementation of lime production investment projects in the localities according to the approved planning; collect suggestions on lime planning before granting approval for new projects; make annual reports on performance to the Ministry of Construction;

Stop granting permits to projects of continued or discontinued manual kilns; build an itinerary, promulgate regulations and carry out removal of continued and discontinued manual kilns according to the planning;

Reinforce the inspection and investigation into the activities of investment and production of lime in the administrative division;

Article 3. Effect

This Decision takes effect since the signing date.

Article 4. Agencies responsible

Ministers, heads of ministerial-level agencies, Governmental agencies, the Presidents of People’s Committees of central-affiliated cities and provinces and relevant agencies shall be responsible for executing this Decision./.

|  | PP THE MINISTER DEPUTY MINISTER Nguyen Tran Nam |
| --- | --- |

APPENDIX 1

LIST OF EXISTING AND NEW INVESTMENT PROJECTS TO 2015 AND FROM 2016 – 2020 WITH INVESTORS IDENTIFIED

| No. | Names of projects or investors | Planned construction sites | Planned zones of raw materials | Capacity (ton/year) | Capacity (ton/year) | Capacity (ton/year) | Capacity (ton/year) | Capacity (ton/year) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Existing | To 2015 | To 2015 | 2016 – 2020 period | 2016 – 2020 period |
|  |  |  |  |  | Additional investment | Accumulation | Additional investment | Accumulation |
| A | MECHANIZED KILNS | MECHANIZED KILNS | MECHANIZED KILNS | 1,100,000 | 2,850,000 | 3,950,000 | 3,460,000 | 7,410,000 |
| 1. | An Hoa Paper Factory | Tuyen Quang Province | Tuyen Quang Province | 100,000 | - | 100,000 | - | 100,000 |
| 2. | Thai Nguyen metallurgy electromechanics Joint Stock Company | Dong Huy District, Thai Nguyen Province | Elephant Mountain Quarry, Dong Huy District, Thai Nguyen Province | In progress | 60,000 | 60,000 | - | 60,000 |
| 3. | Thuong Thanh Limited Liability Company | Chi Lang District, Lang Son Province | Sao Mai Limestone Quarry, Chi Lang District, Lang Son Province | Feasibility Study currently in preparation | 60,000 | 60,000 | - | 60,000 |
| 4. | Luong Son Cement Company | Hoa Binh Province | Lang Rut Limestone Quarry, Tan Vinh Commune, Luong Son District, Hoa Binh Province | Vertical shaft cement kiln technology | 60,000 | 60,000 | - | 60,000 |
| 5. | Huong Hai Limited Liability Company | Hoanh Bo District, Quang Ninh Province | Survey, exploitation within the area of limestone quarries of block II (100 ha), Son Duong Commune, Hoang Bo District, Quang Ninh Province | Construction in progress | 540,000 | 540,000 | 440,000 | 980,000 |
| 6. | SPG joint-stock company | Hoanh Bo and Uong Bi districts, Quang Ninh Province | Limestone Quarry of Hoa Binh and Vu Oai communes, Hoanh Bo and Uong Bi districts, Quang Ninh Province | Feasibility Study currently in preparation | - | - | 300,000 | 300,000 |
| 7. | Dinh Ha Import-Export Joint-Stock Company and Hong Ha Commerce and Transport Joint-Stock Company | Kinh Mon District, Hai Duong Province; Dong Trieu Commune and Uong Bi City, Quang Ninh Province | Limestone Quarry of Hong Thai Tay, Dong Trieu Commune, Uong Bi City; Area of Hoanh Bo, Quang Ninh Province; Kinh Mon District, Hai Duong Province | Converted from manual kilns | 100,000 | 100,000 | 110,000 | 210,000 |
| 8. | DLH industrial lime Joint-Stock Company | Kinh Mon District, Hai Duong Province | DLH Stone Quarry, Thong Nhat Commune, Hoanh Bo District, Quang Ninh Province | Construction in progress | 100,000 | 100,000 | 100,000 | 200,00 |
| 9. | Hoa Phat Steel Joint-Stock Company | Hiep Son Commune, Kinh Mon District, Hai Duong Province | Hiep Son Commune, Kinh Mon District, Hai Duong Province | 150,000 | - | 150,000 | - | 150,000 |
| 10. | Quang Dong Investment Limited Liability Company | Lai Xuan Commune, Thuy Nguyen District, Hai Phong City | Nui Thung Limestone Quarry, Lai Xuan Commune, Thuy Nguyen District, Hai Phong City | Converted from manual kilns | 120,000 | 120,000 | 120,000 | 240,000 |
| 11. | Quang Minh War Invalids Collective Enterprise | Thuy Nguyen District, Hai Phong City | Limestone quarries of Quai Sanh Mountain (upper), Quai Sanh Mountain (Below), Do Mountain, Gia Minh Commune, Hom Dau Moutain, Minh Tan Commune, Thuy Nguyen District, Hai Phong City | Feasibility Study currently in preparation | 100,000 | 100,000 | - | 100,000 |
| 12. | Duc Thai Joint-Stock Company | Thuy Nguyen District, Hai Phong City | Tay Da Kep Limestone Quarry, Lien Khe Commune, Luu Ky Commune, Thuy Nguyen District, Hai Phong City | 150,000 | 100,000 | 250,000 | - | 250,000 |
| 13. | Huong Hai Limited Liability Company | Hai Phong City, Quang Ninh Province | Dong Gia Limestone Quarry, Minh Tan Commune, Sa Gac Quarry, Minh Duc Commune, Thuy Nguyen District, Hai Phong City | Project in progress | 200,000 | 200,000 | 240,000 | 440,000 |
| 14. | Tan Phu Xuan Cement Joint-Stock Company | Thuy Nguyen District, Hai Phong City | Limestone quarries of Cong Da 1, Cong Da 2, stone quarries in Lien Khe H Commune, Thuy Nguyen District, Hai Phong City | Converted from vertical shaft cement kilns | 100,000 | 100,000 | 150,000 | 250,000 |
| 15. | Savina joint-stock company | Thanh Son Commune, Kim Bang District, Ha Nam Province | Thanh Son Commune, Kim Bang District, Ha Nam Province | 60,000 | - | 60,000 | - | 60,000 |
| 16. | Trang An Cement Company | Thanh Liem District, Ha Nam Province | Limestone quarries of T35, T36, Thanh Nghi and Thanh Tan communes, Thanh Liem District, Ha Nam Province | Project in progress | 100,000 | 100,000 | - | 100,000 |
| 17. | Xuan Thanh Investment and Construction Limited Liability Company | Thanh Liem District, Ha Nam Province | Limestone quarries in Thanh Thuy and Thanh Tan communes (46.2 ha), Thanh Liem District, Ha Nam Province | Feasibility Study currently in preparation | 230,000 | 230,000 | 200,000 | 430,000 |
| 18. | Van Xuan Investment Joint-Stock Company | Ky Phu Commune, Nho Quan District, Ninh Binh Province | Ky Phu dolomite limestone quarry, Nho Quan District, granted the exploitation license and Investment Certificate No. 09121000034 dated December 31, 2010 by Ninh Binh Province | In progress | 200,000 | 200,000 | 200,000 | 400,000 |
| 19. | Viet Thang Single-Member Limited Liability Company | Tam Diep Commune, Ninh Binh Province | Nui Chay Limestone Quarry, Nam Son Ward, Tam Diep Commune, Ninh Binh Province | Converted from manual kilns | 100,000 | 100,000 | 100,000 | 200,000 |
| 20. | Truong Thinh Limited Liability Company | Tam Diep Commune, Ninh Binh Province | Stone quarry to the northwest of Long An Mountain, Dong Son Commune, Tam Diep district-level town, Ninh Binh Province | Converted from manual kilns | 60,000 | 60,000 | 60,000 | 120,000 |
| 21. | Vietnam Single-Member Limited Liability Company | Bim Son district-level town, Thanh Hoa Province | Bim Son district-level town, Thanh Hoa Province | 150,000 | - | 150,000 | - | 150,000 |
| 22. | Linh Thanh High-Quality Stone Powder Production Joint-Stock Company | Chau Hoa Commune, Tuyen Hoa District, Quang Binh Province | Stone quarries of Len Minh Cam (63.48 ha), Len Hung and Len Minh (75.23 ha), Chau Hoa Commune, Tuyen Hoa District, Quang Binh Province | In progress | - | - | 350,000 | 350,000 |
| 23. | Dong Bac Coal Mineral Investment Joint-Stock Company | Kim Lo Commune, Tuyen Hoa District, Quang Binh Province | Kim Lu Stone Quarry, Kim Hoa Commune, Tuyen Hoa District, Quang Binh Province | Project in progress | 200,000 | 200,000 | 100,000 | 300,000 |
| 24. | An Phat Mineral Exploitation Investment Joint-Stock Company | Len Giang Area, Trung Hoa Commune, Minh Hoa District, Quang Binh Province | Len Giang dolomite limestone area, Trung Hoa Commune, Minh Hoa District, Quang Binh Province | In progress | 100,000 | 100,000 | 280,000 | 380,000 |
| 25. | Minh Hung Joint-Stock Company | Cam Thanh Commune, Cam Lo, Ta Rung and Huong Hoa districts | Tan Lam Area, Cam Thanh Commune, Cam Lo, Ta Rung and Huong Hoa districts | Currently in possession of vertical shaft cement kilns | 60,000 | 60,000 | - | 60,000 |
| 26. | Chu Lai Soda Production Joint-Stock Company | Quang Nam Province | Thach My 2 Stone Quarry, Nam Giang District, Quang Nam Province | 350,000 | - | 350,000 | - | 350,000 |
| 27. | Hoan Son Investment and Develoment Joint-Stock Company | Ea Sup District, Dak Lak Province | Ban Dao Limestone Quarry, Ea Ie Commune, Ea Sup District | In progress | 150,000 | 150,000 | 150,000 | 300,000 |
| 28. | Thai Bao Saigon Investment Joint-Stock Company | Hon Quan District, Binh Phuoc Province | Limestone quarries of An Phu and Minh Tam communes, Hon Quan District, Binh Phuoc Province | Feasibility Study currently in preparation | 60,000 | 60,000 | 60000 | 120,000 |
| 29. | Tan Thanh My joint-stock company | Ba Ria Vung Tau Province | Ba Ria Vung Tau Province | 40,000 | - | 40,000 | - | 40,000 |
| 30. | Huong Hai Limited Liability Company | Binh An Commune, Kien Luong District, Kien Giang Province | Quarries of Tuc Khoi Moutain, Duong Hoa Commune, Small Mountain, Large Lime Kiln Mountain, Water Mountain, Binh An Commune, Kien Luong District, Kien Giang Province | Construction in progress | 150,000 | 150,000 | 300,000 | 450,000 |
| 31. | Lanh-ke Ha Tien Joint-Stock Company | Binh An Commune, Kien Luong District | Cay Ot Cave Quarry, Binh An Commune, Kien Luong District, Kien Giang Province | Feasibility Study in progress | - | - | 100,000 | 100,000 |
| B | DISCONTINUED MANUAL KILNS | DISCONTINUED MANUAL KILNS | DISCONTINUED MANUAL KILNS | 1,140,000 | - 640,000 | 500,000 | - 500,000 | 0 |
| C | CONTINUED MANUAL KILNS | CONTINUED MANUAL KILNS | CONTINUED MANUAL KILNS | 1,000,000 | 0 | 1,000,000 | -1,000,000 | 0 |
|  | Total | Total | Total | 3,240,000 | 2,170,000 | 5,450,000 | 1,600,000 | 7,410,000 |

APPENDIX 2

LIST OF INVESTMENT PROJECTS AND ZONES OF RAW MATERIALS TO 2015 AND 2016 – 2020 PERIOD WITH INVESTORS UNIDENTIFIED

| No. | Planned sites | Planned zones of raw materials | Capacity (ton/year) | Capacity (ton/year) | Capacity (ton/year) |
| --- | --- | --- | --- | --- | --- |
|  |  |  | To 2015 | Additional investment (2016-2020) | Accumulation to 2020 |
| 1 | Tuyen Quang | Tuyen Quang Province |  | 60,000 | 60,000 |
| 2 | Thai Nguyen | Elephant Mountain Quarry, Dong Hy District, Thai Nguyen Province |  | 60,000 | 60,000 |
|  |  | Limestone quarries in La Hien and Lau Thuong communes, Vo Nhai District |  | 60,000 | 60,000 |
| 3 | Yen Bai | Limestone quarries in Mong Son Commune, Yen Binh District |  | 60,000 | 60,000 |
| 4 | Lao Cai | Cam Duong Quarry, Bao Thang District |  | 60,000 | 60,000 |
| 5 | Bac Giang | Limestone quarries in Dong Tan Commune, Huu Lung District, Lang Son Province | 100,000 |  | 100,000 |
| 6 | Lang Son | Limestone quarries in Dong Tan Commune, Huu Lung and Sa Khao districts, Lang Son Province | 100,000 |  | 100,000 |
| 7 | Hoa Binh | Lang Rut Limestone Quarry, Tan Vinh Commune, Luong Son District, Hoa Binh Province |  | 60,000 | 60,000 |
| 8 | Dien Bien | Muong Ang, Dien Bien, Tuan Giao |  | 60,000 | 60,000 |
| 9 | Quang Ninh | Limestone quarries of Son Duong and Thong Nhat communes, Hoanh Bo District, limestone quarries of Hong Thai Tay, Dong Trieu District, Phuong Nam Ward, Uong Bi City, Quang Ninh Province |  | 120,000 | 120,000 |
|  |  | Stone quarries of Vu Quai and Hoa Binh communes, Hoanh Bo District |  | 120,000 | 120,000 |
| 10 | Hai Phong | Limestone quarries in southwest of Block B, Trai Son Moutain, An Son (16.98 ha), Lai Xuan, Gia Minh, Gia Duc, Minh Tan, Minh Duc, Lien Khe and Luu Ky communes, Thuy Nguyen District, Hai Phong City |  | 120,000 | 120,000 |
| 11 | Hai Duong | Toad Mountain, Elephant Mountain, Peacock Mountain, Demon Mountain, Kinh Mon District |  | 60,000 | 60,000 |
| 12 | Ha Nam | Limestone quarries of Thanh Son Commune, Kim Bang District, Thanh Nghi, Thanh Tan and Thanh Thuy communes, Thanh Liem District |  | 60,000 | 60,000 |
| 13 | Ninh Binh | - Ky Phu dolomite limestone quarries, Nho Quan District - Thung Chuong Stone Quarry, Ngoc Cao Village , Duc Long Commune, Nho Quan District, Ninh Binh Province - Limestone quarries of Yen Mo, Nho Quan and Gia Vien districts and Tam Diep district-level town - Stone quarry to the northwest of Long An Mountain, Dong Son Commune, Tam Diep district-level town, Ninh Binh Province | 60,000 | 60,000 | 120,000 |
| 14 | Thanh Hoa | Limestone quarries of Bim Son district-level town and Dong Son District, Thanh Hoa Province |  | 60,000 | 60,000 |
| 15 | Nghe An | Limestone quarries of Quynh Luu, Tan Ky, Do Luong and Anh Son districts | 60,000 | 60,000 | 120,000 |
| 16 | Binh Phuoc | Limestone quarries of An Phu and Minh Tam communes, Hon Quan and Binh Long districts |  | 60,000 | 80,000 |
| 17 | Kien Giang | Cay Ot Cave Quarry, Binh An Commune, Kien Luong District, Kien Giang Province |  | 60,000 | 60,000 |
|  | Nationwide |  | 350,000 | 1,200,000 | 1,540,000 |

APPENDIX 3

LIST OF LIMESTONE MINERAL QUARRIES SUPPLYING RAW MATERIALS FOR LIME PRODUCTION

| No. | Name of quarry | Name of quarry | Geographic positions | Coordinates | Coordinates | Coordinates | Quality | Deposits (million m3) Area (ha) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | X | X | Y |  |  |
| Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 | Part 1. List of limestone quarries under the planning enclosed with the Prime Minister’ Decision No. 45/QĐ- TTg dated January 09, 2012 |
| 1 | Dong Gia Mountain | Minh Tan Commune, Thuy Nguyen District, Hai Phong City | Minh Tan Commune, Thuy Nguyen District, Hai Phong City | 2320740451 363598453 2320760439 363958478 2320530414 364198487 2320380405 364168479 2320460409 363859461 2320450435 363518438 2320740451 363598453 | 2320740451 363598453 2320760439 363958478 2320530414 364198487 2320380405 364168479 2320460409 363859461 2320450435 363518438 2320740451 363598453 | 2320740451 363598453 2320760439 363958478 2320530414 364198487 2320380405 364168479 2320460409 363859461 2320450435 363518438 2320740451 363598453 |  | 17.4 ha |
| 2 | Tay Da Kep | Lien Khe and Luu Ky communes, Thuy Nguyen District, Hai Phong City | Lien Khe and Luu Ky communes, Thuy Nguyen District, Hai Phong City | 23230933 59419822 23229229 59403450 23227642 59407914 23227559 59416680 23229163 59428089 23228200 67234884 23231598 67241881 | 23230933 59419822 23229229 59403450 23227642 59407914 23227559 59416680 23229163 59428089 23228200 67234884 23231598 67241881 | 23230933 59419822 23229229 59403450 23227642 59407914 23227559 59416680 23229163 59428089 23228200 67234884 23231598 67241881 |  | 11.ha |
| 3 | Bac Hang Giong Lo (T34) | Thanh Tan, Thanh Nghi communes, Thanh Liem District, Ha Nam Province | Thanh Tan, Thanh Nghi communes, Thanh Liem District, Ha Nam Province | 2260838.80 591595.06 2260784.00 591857.23 2260566.42 591972.51 2260390.53 591554.15 2260647.96 591392.35 | 2260838.80 591595.06 2260784.00 591857.23 2260566.42 591972.51 2260390.53 591554.15 2260647.96 591392.35 | 2260838.80 591595.06 2260784.00 591857.23 2260566.42 591972.51 2260390.53 591554.15 2260647.96 591392.35 |  | 15 ha |
| 4 | T34 Limestone, Mo Bo Mountain | Thanh Nghi Commune, Thanh Liem District, Ha Nam Province | Thanh Nghi Commune, Thanh Liem District, Ha Nam Province | 2260299.19 591538.75 2260430.13 591895.18 2260143.63 591990.85 2260071.32 591697.64 | 2260299.19 591538.75 2260430.13 591895.18 2260143.63 591990.85 2260071.32 591697.64 | 2260299.19 591538.75 2260430.13 591895.18 2260143.63 591990.85 2260071.32 591697.64 |  | 9.4 ha |
| 5 | Limestone of Block II | Son Duong Commune, Hoanh Bo District, Quang Ninh Province | Son Duong Commune, Hoanh Bo District, Quang Ninh Province | 2331127 709334 2331201 710063 2331024 710766 2330466 710867 2330154 710763 | 2331127 709334 2331201 710063 2331024 710766 2330466 710867 2330154 710763 | 2331127 709334 2331201 710063 2331024 710766 2330466 710867 2330154 710763 | CaO: 54,36; MgO: 0,42 | 41.4 ha |
| 6 | Limestone of Block V | Thong Nhat Commune, Hoanh Bo District, Quang Ninh Province | Thong Nhat Commune, Hoanh Bo District, Quang Ninh Province | 2330667 713627 2330817 714752 2329817 714752 2329667 713677 | 2330667 713627 2330817 714752 2329817 714752 2329667 713677 | 2330667 713627 2330817 714752 2329817 714752 2329667 713677 | Limestone used for production of hi-tech lime powder | 100 |
| 7 | Kim Lu | Kim Hoa Commune, Tuyen Hoa District | Kim Hoa Commune, Tuyen Hoa District | 1984.962 1984.444 1983.806 1983.567 1983.999 1984.419 1984.167 1984.322 1984.352 1984.609 | 1984.962 1984.444 1983.806 1983.567 1983.999 1984.419 1984.167 1984.322 1984.352 1984.609 | 602.657 603.644 603.774 603.467 603.086 603.125 603.343 603.387 603.141 602.655 | Quality for lime production ensured by Dong Bac Investment Joint-Stock Company | 62.22 ha |
| 8 | Kim Lu | Kim Hoa Commune, Tuyen Hoa District, Quang Binh Province | Kim Hoa Commune, Tuyen Hoa District, Quang Binh Province | Longitude: 105o59’00- Lattitude: 17o55’40- | Longitude: 105o59’00- Lattitude: 17o55’40- | Longitude: 105o59’00- Lattitude: 17o55’40- | CaO: 46,73 – 51,25; MgO: 0,8 – 3,1 | 62.4 ha |
| 9 | An Phu | An Phu Commune, Binh Long District, Binh Phuoc District | An Phu Commune, Binh Long District, Binh Phuoc District | 1291535 664366 1291524 666309 1290002 665519 1290002 663029 | 1291535 664366 1291524 666309 1290002 665519 1290002 663029 | 1291535 664366 1291524 666309 1290002 665519 1290002 663029 | CaO: 49,59 MgO: 2,65 | 343 ha |
| 10 | An Phu | An Phu Commune, Hon Quang District, Binh Phuoc District | An Phu Commune, Hon Quang District, Binh Phuoc District | X: 1292365 to 1292095 Y: 663189 to 662618 | X: 1292365 to 1292095 Y: 663189 to 662618 | X: 1292365 to 1292095 Y: 663189 to 662618 |  | 120 ha |
| 11 | Minh Tam | Minh Tam Commune, Hon Quang District, Binh Phuoc District | Minh Tam Commune, Hon Quang District, Binh Phuoc District | X: 1289951 to 1289290 Y: 661173 to 660720 | X: 1289951 to 1289290 Y: 661173 to 660720 | X: 1289951 to 1289290 Y: 661173 to 660720 |  | 80 ha |
| 12 | South of Khoe La Mountain | Binh An Commune, Kien Luong District, Kien Giang Province | Binh An Commune, Kien Luong District, Kien Giang Province | 1128118 454946 1128171 455053 1128175 455065 1128133 455024 1127973 455084 1127885 455221 1127869 455155 1127843 455058 1127827 454985 1127795 454857 1127888 454884 1127795 454921 | 1128118 454946 1128171 455053 1128175 455065 1128133 455024 1127973 455084 1127885 455221 1127869 455155 1127843 455058 1127827 454985 1127795 454857 1127888 454884 1127795 454921 | 1128118 454946 1128171 455053 1128175 455065 1128133 455024 1127973 455084 1127885 455221 1127869 455155 1127843 455058 1127827 454985 1127795 454857 1127888 454884 1127795 454921 |  | 4.955 ha and 3.213 million m3 surveyed |
| 13 | South of Khoe La Mountain | Binh An Commune, Kien Luong District, Kien Giang Province | Binh An Commune, Kien Luong District, Kien Giang Province | 1128222 454902 1128264 455099 1128118 454916 1128171 455053 1128175 455065 | 1128222 454902 1128264 455099 1128118 454916 1128171 455053 1128175 455065 | 1128222 454902 1128264 455099 1128118 454916 1128171 455053 1128175 455065 |  | 2.499 ha and 1.187 million m3 surveyed |
| 14 | Tuc Khoi Moutain | X. Duong Hoa Commune, Kien Luong District, Kien Giang Province | X. Duong Hoa Commune, Kien Luong District, Kien Giang Province | X: 1139499.69 to 1139348.00 Y: 454140,00 to 454466.00 | X: 1139499.69 to 1139348.00 Y: 454140,00 to 454466.00 | X: 1139499.69 to 1139348.00 Y: 454140,00 to 454466.00 | CaO: 52,74; MgO: 1,12 | 21.75 exploited |
| 15 | Large Lime Kiln | Binh An Commune, Kien Luong District, Kien Giang Province | Binh An Commune, Kien Luong District, Kien Giang Province | 1127262.67 511496.62 1127270.42 511654.76 1127302.24 511627.34 1127466.63 511753.58 1127539.13 511745.27 1127524.99 511476.32 | 1127262.67 511496.62 1127270.42 511654.76 1127302.24 511627.34 1127466.63 511753.58 1127539.13 511745.27 1127524.99 511476.32 | 1127262.67 511496.62 1127270.42 511654.76 1127302.24 511627.34 1127466.63 511753.58 1127539.13 511745.27 1127524.99 511476.32 |  | 7 ha exploited |
| 16 | Small Mountain | Binh An Commune, Kien Luong District, Kien Giang Province | Binh An Commune, Kien Luong District, Kien Giang Province | X: 1128706.00 to 1128757.18 Y: 458873.00 to 458810,00 | X: 1128706.00 to 1128757.18 Y: 458873.00 to 458810,00 | X: 1128706.00 to 1128757.18 Y: 458873.00 to 458810,00 |  | 5,0 ha exploited |
| 17 | Thanh My 2 | Thanh My Commune, Nam Giang District, Quang Nam Province | Thanh My Commune, Nam Giang District, Quang Nam Province | Block 1 (54.63 ha) 1741.585 1741.585 1741.946 1741.946 1741.662 1741.662 1741.317 1741.317 Block 2 (57 ha) 1741.738 1741.738 1742.082 1742.082 1742.610 1742.610 1742.421 1742.421 | Block 1 (54.63 ha) 1741.585 1741.585 1741.946 1741.946 1741.662 1741.662 1741.317 1741.317 Block 2 (57 ha) 1741.738 1741.738 1742.082 1742.082 1742.610 1742.610 1742.421 1742.421 | Block 1 (54.63 ha) 1741.585 1741.585 1741.946 1741.946 1741.662 1741.662 1741.317 1741.317 Block 2 (57 ha) 1741.738 1741.738 1742.082 1742.082 1742.610 1742.610 1742.421 1742.421 | Limestone serving the industries (TB: CaO: 51.12; MgO: 0.62) | C2+P: 900 million m3 116.63 ha |
| 18 | Ma Cooih | Dong Giang District, Quang Nam Province | Dong Giang District, Quang Nam Province | 1756385 792384 1756044 791216 1755738 791111 1755469 790580 | 1756385 792384 1756044 791216 1755738 791111 1755469 790580 | 1756385 792384 1756044 791216 1755738 791111 1755469 790580 | Limestone serving the industries (TB: CaO: 51.12; MgO: 0.62) | P: 121.15 million m3 83.57 ha |
| Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 | Part 2. List of limestone quarries according to the Prime Minister’ Decision No. 105/2008/QĐ-TTg dated July 21, 2008 and Decision No. 1065/QĐ-TTg dated July 09, 2010 |
| Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong |
| 1 | Cong Da 2 Mountain | Lien Khe Commune, Thuy Nguyen District | Lien Khe Commune, Thuy Nguyen District | X: 2324.150; Y: 357.250 | X: 2324.150; Y: 357.250 | X: 2324.150; Y: 357.250 |  | P: 3.87 |
| Ha Nam | Ha Nam | Ha Nam | Ha Nam | Ha Nam | Ha Nam | Ha Nam | Ha Nam | Ha Nam |
| 1 | Bac Tan Lang (K2) | Tuong Linh, Tan Son communes, Kim Bang District | Tuong Linh, Tan Son communes, Kim Bang District |  |  |  | CaO: 52.69; MgO: 2.39 | P: 65.26 |
| 2 | Southwest of Dong Bung (K6) | Kha Phong, Tan Son communes, Kim Bang District | Kha Phong, Tan Son communes, Kim Bang District |  |  |  | CaO: 53.3 ; MgO: 2.05 | P: 52.7 |
| 3 | Do Le (K11) | Kha Phong, Lien Son and Ba Sao communes, Kim Bang District | Kha Phong, Lien Son and Ba Sao communes, Kim Bang District |  |  |  | CaO: 53.8; MgO: 01.51 | P: 15.345 |
| 4 | Tay But Son (K22) | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province |  |  |  | CaO: 52.69; MgO: 2.39 | P: 393.76 (the Service of Construction) |
| 5 | Thung Ham Que (K35) | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province |  |  |  |  | P: 369 |
| 6 | Thung Canh Noi (K36) | Thanh Son Commune, Kim Bang District, Ha Nam Province | Thanh Son Commune, Kim Bang District, Ha Nam Province |  |  |  |  | P: 58 |
| 7 | Thung Be (K38) | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province |  |  |  | CaO: 54.42; MgO: 1.3 | P: 453 |
| 8 | Tay Thon Vong (K7) | Kha Phong, Tan Son communes, Kim Bang District | Kha Phong, Tan Son communes, Kim Bang District |  |  |  |  | P: 11.7 |
| 9 | Thanh Son (K22) | Thanh Son Commune, Kim Bang District, Ha Nam Province | Thanh Son Commune, Kim Bang District, Ha Nam Province | Longitude: 105o51'34- Lattitude: 20o 31'00" | Longitude: 105o51'34- Lattitude: 20o 31'00" | Longitude: 105o51'34- Lattitude: 20o 31'00" | CaO: 53.8; MgO: 01.51 | Total: 415.428 of which: C1+ C2: 163.8 |
| 10 | Tay Thung Hop (T12) | Thanh Thuy Commune, Thanh Liem District | Thanh Thuy Commune, Thanh Liem District |  |  |  | CaO: 54.3 – 54.9; MgO: 0.36 -1.17 | P: 111.7 |
| 11 | Tay Bac Thung Duoc (T18) | Thanh Thuy Commune, Thanh Liem District | Thanh Thuy Commune, Thanh Liem District |  |  |  | CaO: 52.5 – 53.9; MgO: 1.28 – 1.8 | P: 24.0 |
| 12 | Sky Gate (T20) | Thanh Thuy Commune, Thanh Liem District | Thanh Thuy Commune, Thanh Liem District |  |  |  | CaO : 52.2; MgO : 1.4 | P: 97.0 |
| 13 | Nam Thung (T22) | Thanh Thuy, Thanh Tan communes, Thanh Liem District, Ha Nam Province | Thanh Thuy, Thanh Tan communes, Thanh Liem District, Ha Nam Province |  |  |  | CaO: 50.57; MgO: 1.64 | P: 78.3 |
| 14 | Dong Thon (T48) | Kien Khe Commune, Thanh Liem District | Kien Khe Commune, Thanh Liem District |  |  |  | CaO: 52.5-53.9; MgO: 1.28-1.8 | P: 21.3 |
| 15 | Thanh Nghi (T36) | Thanh Thuy Commune, Thanh Liem District | Thanh Thuy Commune, Thanh Liem District | Longitude: 105o52'00 - Lattitude: 20o27'05 | Longitude: 105o52'00 - Lattitude: 20o27'05 | Longitude: 105o52'00 - Lattitude: 20o27'05 | CaO : 52.2; MgO : 1.4 |  |
| 16 | Dong Ao | Thanh Thuy Commune, Thanh Liem District | Thanh Thuy Commune, Thanh Liem District | Longitude: 105o52'00 - Lattitude: 20o29"30" | Longitude: 105o52'00 - Lattitude: 20o29"30" | Longitude: 105o52'00 - Lattitude: 20o29"30" | CaO: 52.69; MgO: 2.39 | C2: 12.43 |
| 17 | Moc Mountain | Thanh Tan Commune, Thanh Liem District, Ha Nam Province | Thanh Tan Commune, Thanh Liem District, Ha Nam Province | Longitude: 105o53;00 - Lattitude: 20o26'00" | Longitude: 105o53;00 - Lattitude: 20o26'00" | Longitude: 105o53;00 - Lattitude: 20o26'00" | CaO: 53.3; MgO: 2.05 | P: 5.388 |
| 18 | Dong Thung Da Lien (K20) | Lien Son Commune, Kim Bang District, Ha Nam Province | Lien Son Commune, Kim Bang District, Ha Nam Province |  |  |  | CaO: 53.47; MgO: 0.41 | P: 237.94 |
| 19 | Dong Xom Suoi Ngang (K15) | Lien Son and Ba Sao communes, Kim Bang District, Ha Nam Province | Lien Son and Ba Sao communes, Kim Bang District, Ha Nam Province |  |  |  | CaO: 54.42; MgO: 1.3 | P: 77 |
| 20 | But Phong (K16) | Lien Son Commune, Kim Bang District, Ha Nam Province | Lien Son Commune, Kim Bang District, Ha Nam Province |  |  |  |  | 324.32; of which: B+C1+C2: 130.75; P:193,57 |
| 21 | Nui Hang But (T10) | Thanh Thuy, Thanh Tan communes, Thanh Liem District, Ha Nam Province | Thanh Thuy, Thanh Tan communes, Thanh Liem District, Ha Nam Province |  |  |  | CaO: 54.05; MgO: 0.11 | P: 73.4 |
| 22 | Thung Dong (K30) | Lien Son Commune, Kim Bang District, Ha Nam Province | Lien Son Commune, Kim Bang District, Ha Nam Province |  |  |  | CaO: 54.42; MgO: 1.3 | P: 36.7 |
| 23 | Tay Thung Don (T2) | Kien Khe Commune, Kim Bang District, Ha Nam Province | Kien Khe Commune, Kim Bang District, Ha Nam Province |  |  |  | CaO: 53.47; MgO: 0.41 | P: 41 |
| 24 | Thung Da Lien (K19) | Lien Son and Ba Sao communes, Kim Bang District, Ha Nam Province | Lien Son and Ba Sao communes, Kim Bang District, Ha Nam Province |  |  |  | CaO: 50-54; MgO: 0.7-1.5 | P: 169.6 |
| 25 | Nam Thung Tien Sinh (K33) | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province | Thanh Son, Lien Son communes, Kim Bang District, Ha Nam Province |  |  |  | CaO: 53.47; MgO: 0.41 | P: 242 |
| 26 | Doc Ba Chom (K27) | Ba Sao Commune, Kim Bang District, Ha Nam Province | Ba Sao Commune, Kim Bang District, Ha Nam Province |  |  |  | CaO: 53.3 ; MgO: 2.05 | P: 110 |
| Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh |
| 1 | Thien Duong | Ninh Van Commune, Hoa Lu District | Ninh Van Commune, Hoa Lu District |  |  |  | CaO: 53.27; MgO: 1.3 | Not available |
| 2 | Ky Phu, Phu Long communes | Ky Phu, Phu Long communes, Nho Quan District | Ky Phu, Phu Long communes, Nho Quan District | Longitude: 105o46'30- Lattitude:20o20'30- | Longitude: 105o46'30- Lattitude:20o20'30- | Longitude: 105o46'30- Lattitude:20o20'30- | CaO: 53 - 54; MgO: 0.55 -1.5 | Total: 240 (of which C : 40) |
| 3 |  | Within Yen Mo Limestone area | Within Yen Mo Limestone area |  |  |  |  | Not available |
| 4 | Gia Thanh | Gia Thanh Commune, Gia Vien District | Gia Thanh Commune, Gia Vien District |  |  |  |  | P: 70 million m3 ~ 195 million ton |
| Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai |
| 1 | Cam Duong | Cam Duong Commune, Bao Thang District | Cam Duong Commune, Bao Thang District | Longitude: 103o59'12- Lattitude: 22o25'40" | Longitude: 103o59'12- Lattitude: 22o25'40" | Longitude: 103o59'12- Lattitude: 22o25'40" | CaO: 47- 53; MgO: <3.5 | Total: 7.697; C1: 1.085; C2: 2.912; P: 3,7 |
| 2 | Tien Phong | Phong Hai commune-level town | Phong Hai commune-level town | Longitude: 103o59'12"; Lattitude: 22o25'40" | Longitude: 103o59'12"; Lattitude: 22o25'40" | Longitude: 103o59'12"; Lattitude: 22o25'40" | CaO: 53; MgO: 1.4 | P : 6.2 |
| 3 | Ma Tong | Pha Long Commune, Muong Khuong District | Pha Long Commune, Muong Khuong District | Longitude: 103o12'00- Lattitude: 22o45'00- | Longitude: 103o12'00- Lattitude: 22o45'00- | Longitude: 103o12'00- Lattitude: 22o45'00- |  | P: 500 |
| 4 | Van Ban | Khanh Yen Trung Commune, Van Ban District | Khanh Yen Trung Commune, Van Ban District | Longitude: Lattitude: | Longitude: Lattitude: | Longitude: Lattitude: |  | P: 10 |
| 5 | Phong Nien | Phong Nien Commune, Bao Thang District | Phong Nien Commune, Bao Thang District |  |  |  |  | 36.96 ha |
| Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son |
| 1 | Co Stream | Hoa Lac Commune, Huu Lung District | Hoa Lac Commune, Huu Lung District | Longitude: 106o27'00- Lattitude: 22o33'00- | Longitude: 106o27'00- Lattitude: 22o33'00- | Longitude: 106o27'00- Lattitude: 22o33'00- | Cao: 55.7; MgO: 3.23 | P: > 100 |
| 2 | Dong Lai | X. Cai Kinh Commune, Huu Lung District | X. Cai Kinh Commune, Huu Lung District | Longitude :106o22'25" Lattitude: 21o32'30" | Longitude :106o22'25" Lattitude: 21o32'30" | Longitude :106o22'25" Lattitude: 21o32'30" | CaO: 52 - 54; MgO: 1-1.5 | P: > 100 |
| 3 | Minh Tien | X. Minh Tien Commune, Huu Lung District | X. Minh Tien Commune, Huu Lung District | Kinh độ: 106o16'20" Lattitude: 21o33'20" | Kinh độ: 106o16'20" Lattitude: 21o33'20" | Kinh độ: 106o16'20" Lattitude: 21o33'20" | CaO: 50 - 53; MgO: 0.4-1.5 | P: > 1.440 |
| 4 | Quan Thanh | Chi Lang Commune, Chi Lang District | Chi Lang Commune, Chi Lang District | Longitude: 106o31'14"; Lattitude: 21o36'29" | Longitude: 106o31'14"; Lattitude: 21o36'29" | Longitude: 106o31'14"; Lattitude: 21o36'29" | CaO: 54,4 ; MgO: 04- 0.5 | P: 210 |
| Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang | Tuyen Quang |
| 1 | Cam Bon | Da Vi Commune, Na Hang District | Da Vi Commune, Na Hang District | Longitude: 105o35'30" Lattitude: 22o29'30" | Longitude: 105o35'30" Lattitude: 22o29'30" | Longitude: 105o35'30" Lattitude: 22o29'30" | Cao: 53.28; MgO: 1.34 | P: 80 |
| 2 | Bac Lang Mai | Thuong Lam Commune, Na Hang District | Thuong Lam Commune, Na Hang District | Longitude: 105o54'44" Lattitude: 21o29'30" | Longitude: 105o54'44" Lattitude: 21o29'30" | Longitude: 105o54'44" Lattitude: 21o29'30" | Cao: 54.4; MgO: 1 | P: 47.2 |
| 3 | Binh Ca | Thai Binh Commune, Yen Son District | Thai Binh Commune, Yen Son District | Longitude: 105o15'50" Lattitude: 21o45'44" | Longitude: 105o15'50" Lattitude: 21o45'44" | Longitude: 105o15'50" Lattitude: 21o45'44" | Cao: 53.99 – 55.8; MgO: 0.8 – 1.52 | P: 16.25 |
| 4 | Da Nang | H. Son Duong District | H. Son Duong District | Longitude: 105o19’00" Lattitude: 21o44'30" | Longitude: 105o19’00" Lattitude: 21o44'30" | Longitude: 105o19’00" Lattitude: 21o44'30" | CaO: 48,79 – 53.95; MgO: 1.17 – 1.56 | C1+C2+P: 500 |
| 5 | Y Nhan | Phuc Ung Commune, Son Duong District | Phuc Ung Commune, Son Duong District | Longitude: 105o21'00" Lattitude: 21o41'20" | Longitude: 105o21'00" Lattitude: 21o41'20" | Longitude: 105o21'00" Lattitude: 21o41'20" | CaO: 51.36 – 52.78; MgO: 0.7 – 1.86 | C1: 6.5 P2: 17 |
| 6 | Bac Ban | Cach Xa Commune, Ham Yen District | Cach Xa Commune, Ham Yen District | Longitude: 10o56'02" Lattitude: 22o14'16" | Longitude: 10o56'02" Lattitude: 22o14'16" | Longitude: 10o56'02" Lattitude: 22o14'16" | CaO: 55.10; MgO: 0.67 | P: 100 |
| 7 | Lang Chay | Tan Tien Commune, Yen Son District | Tan Tien Commune, Yen Son District | Longitude: 10o16'00" Lattitude: 21o51'37" | Longitude: 10o16'00" Lattitude: 21o51'37" | Longitude: 10o16'00" Lattitude: 21o51'37" | CaO: 50.4 - 56; MgO: 0.8 – 3.4 | Point of mineral |
| 8 | Thuong Am | Thuong Am Commune, Son Duong District | Thuong Am Commune, Son Duong District | Longitude: 105o20'30" Lattitude: 21o44'10" | Longitude: 105o20'30" Lattitude: 21o44'10" | Longitude: 105o20'30" Lattitude: 21o44'10" | CaO: 51.3 – 52.7; MgO: | Point of mineral |
| 9 | Doi Binh | Doi Binh Commune, Yen Son District | Doi Binh Commune, Yen Son District | Longitude: 105o12'40" Lattitude: 21o41'54" | Longitude: 105o12'40" Lattitude: 21o41'54" | Longitude: 105o12'40" Lattitude: 21o41'54" | CaO: 50.32 – 51.22; MgO: 01.81 – 3.1 | Point of mineral |
| 10 | Ao Sen | Thien Ke Commune, Son Duong District | Thien Ke Commune, Son Duong District |  |  |  | CaO: 51.6 - 52.84; MgO: 1.96 - 2.2 | Point of mineral |
| YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI | YÊN BÁI |
| 1 | Lang Can | Mong Son Commune, Yen Binh District | Mong Son Commune, Yen Binh District | Longitude: 104o53'24" Lattitude: 21o53'45" | Longitude: 104o53'24" Lattitude: 21o53'45" | Longitude: 104o53'24" Lattitude: 21o53'45" | CaO: 55.12 - 55.93; MgO: 0,09 -0.93 | C1+ C2: 74.52 |
| 2 | My Gia II | My Gia Commune, Yen Binh District | My Gia Commune, Yen Binh District | Longitude: 104o56'50" Lattitude: 21o56'30" | Longitude: 104o56'50" Lattitude: 21o56'30" | Longitude: 104o56'50" Lattitude: 21o56'30" |  | Point of mineral |
| 3 | Bong Sat | An Phu Commune, Luc Yen District | An Phu Commune, Luc Yen District | Longitude: 104o48'00" Lattitude: 21o57'40" | Longitude: 104o48'00" Lattitude: 21o57'40" | Longitude: 104o48'00" Lattitude: 21o57'40" | CaO: 46 - 52.3; MgO: 0.72 - 2.3; | P : 3.4 |
| 4 | Ba Khe | Suoi Bu Commune, Van Chan District | Suoi Bu Commune, Van Chan District | Longitude: 104o38'00" Lattitude: 21o33'45" | Longitude: 104o38'00" Lattitude: 21o33'45" | Longitude: 104o38'00" Lattitude: 21o33'45" | CaO: 46 - 52.3; MgO: 0.72 - 2.3; | Point of mineral |
| 5 | Nui Lang | An Phu Commune, Luc Yen District | An Phu Commune, Luc Yen District | Longitude: 104o50'51" Lattitude: 21o58'55" | Longitude: 104o50'51" Lattitude: 21o58'55" | Longitude: 104o50'51" Lattitude: 21o58'55" | CaO: 50 -54; MgO: 1.8; | Point of potentia mineral |
| 6 | Lang Du | Cam Nhan Commune, Yen Binh District | Cam Nhan Commune, Yen Binh District | Longitude: 104o58'06" Lattitude: 21o58'17" | Longitude: 104o58'06" Lattitude: 21o58'17" | Longitude: 104o58'06" Lattitude: 21o58'17" | CaO: 55.29; MgO: 0.52; | Point of large forecast natural resource mineral |
| 7 | An Phu | An Phu Commune, Luc Yen District | An Phu Commune, Luc Yen District | Longitude: 104o50'24" Lattitude: 21o58'34" | Longitude: 104o50'24" Lattitude: 21o58'34" | Longitude: 104o50'24" Lattitude: 21o58'34" | CaO: 51.67; MgO: 3.7; | Point of large forecast natural resource mineral |
| Dien Bien | Dien Bien | Dien Bien | Dien Bien | Dien Bien | Dien Bien | Dien Bien | Dien Bien | Dien Bien |
| 1 | Pa Thom | H. Dien Bien District | H. Dien Bien District |  |  |  |  | Unidentified |
| 2 | Muong Ang | Ang Cang Commune, Tuan Giao District | Ang Cang Commune, Tuan Giao District | Longitude: 102o55'35" Lattitude: 22o14'50" | Longitude: 102o55'35" Lattitude: 22o14'50" | Longitude: 102o55'35" Lattitude: 22o14'50" |  | P: 20.655 |
| 3 | Ta Sin Thang | Ta Phin Commune, Tua Chua District | Ta Phin Commune, Tua Chua District | Longitude: 103o21'28" Lattitude: 22o21'20" | Longitude: 103o21'28" Lattitude: 22o21'20" | Longitude: 103o21'28" Lattitude: 22o21'20" | CaO: ; MgO: | Point of mineral |
| 4 | Ka La Vo | Hua Ngai Commune, Muong Tra District | Hua Ngai Commune, Muong Tra District | Longitude: 103o12'12" Lattitude: 21o57'13" | Longitude: 103o12'12" Lattitude: 21o57'13" | Longitude: 103o12'12" Lattitude: 21o57'13" | CaO: 55.34; MgO: 55.62 | Point of mineral |
| 5 | Trung Thu | Trung Thu Commune, Tua Chua District | Trung Thu Commune, Tua Chua District | Longitude:103o19'30" Lattitude: 21o56'35" | Longitude:103o19'30" Lattitude: 21o56'35" | Longitude:103o19'30" Lattitude: 21o56'35" | CaO: 51.1; MgO: 0.7- 2.5 | Point of mineral |
| 6 | Sa Long | Hoi Leng Commune, Muong Tra District | Hoi Leng Commune, Muong Tra District | Longitude: 103o07'56" Lattitude: 21o49'29" | Longitude: 103o07'56" Lattitude: 21o49'29" | Longitude: 103o07'56" Lattitude: 21o49'29" | CaO: 49.91 - 54.82; MgO: 0,04 -0.1 | Point of mineral |
| 7 | Na Pheo | Muong Mon Commune, Muong Tra District | Muong Mon Commune, Muong Tra District | Longitude: 103o04'15" Lattitude: 21o44'15" | Longitude: 103o04'15" Lattitude: 21o44'15" | Longitude: 103o04'15" Lattitude: 21o44'15" | CaO: 49.63 - 55.24; MgO: 0,04 - 3.6 | Point of mineral |
| 8 | Pu Nhung | Pu Nhung Commune, Tuan Giao District | Pu Nhung Commune, Tuan Giao District | Longitude: 103o28'09" Lattitude: 210o42'45" | Longitude: 103o28'09" Lattitude: 210o42'45" | Longitude: 103o28'09" Lattitude: 210o42'45" | CaO: 53 - 54.96; MgO: 0,04 - 3.6 | Point of mineral P: 8.700 |
| Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh | Hoa Binh |
| 1 | Lang Rut | X. Tan Vinh Commune, Luong Son District | X. Tan Vinh Commune, Luong Son District | Longitude: 105o33'00"; Lattitude: 20o52'20" | Longitude: 105o33'00"; Lattitude: 20o52'20" | Longitude: 105o33'00"; Lattitude: 20o52'20" | CaO: 52.92. MgO: 0.50 | C2: 17.54 |
| 3 | Trieu Thuy | X. My Hoa Commune, Kim Boi District | X. My Hoa Commune, Kim Boi District | Longitude: 105o36'33"; Lattitude: 20o34'06"’ | Longitude: 105o36'33"; Lattitude: 20o34'06"’ | Longitude: 105o36'33"; Lattitude: 20o34'06"’ | CaO: 53.7, MgO: 0.8 | P: 83.5 |
| 3 | Dong Dang | Cao Duong Commune, Luong Son District | Cao Duong Commune, Luong Son District | Unidentified | Unidentified | Unidentified |  | P2: 189 area: 225 ha |
| 4 | Dong Tam | Dong Tam Commune, Lac Thuy District | Dong Tam Commune, Lac Thuy District | Unidentified | Unidentified | Unidentified |  | P2: 189 |
| Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials | Phần 3. Part 3. List of limestone quarries used as conventional building materials |
| Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong | Hai Phong |
| 1 | Cong Da 1 Mountain | Lien Khe Commune, Thuy Nguyen District | Lien Khe Commune, Thuy Nguyen District | X: 2324.330; Y: 357.700 | X: 2324.330; Y: 357.700 | X: 2324.330; Y: 357.700 |  | P; 5.72 |
| 2 | Lakeshore Mountain | Lien Khe Commune, Thuy Nguyen District | Lien Khe Commune, Thuy Nguyen District | X: 2324.470; Y: 359.900 | X: 2324.470; Y: 359.900 | X: 2324.470; Y: 359.900 |  | P: 4.86 |
| 3 | Southwestern Mountain in Block B, Trai Son B Mountain | An Son Commune, Thuy Nguyen District | An Son Commune, Thuy Nguyen District | City area provided with conventional building materials | City area provided with conventional building materials | City area provided with conventional building materials | CaO: 53.6; MgO: 1.76 |  |
| 4 | Pig Skin Mountain | Minh Tan Commune, Thuy Nguyen District, Hai Phong City | Minh Tan Commune, Thuy Nguyen District, Hai Phong City | 2321564.155 598052.661 2321506.563 598223.453 2321378.732 598104.457 2321322.218 598133.266 2321301.208 597864.381 | 2321564.155 598052.661 2321506.563 598223.453 2321378.732 598104.457 2321322.218 598133.266 2321301.208 597864.381 | 2321564.155 598052.661 2321506.563 598223.453 2321378.732 598104.457 2321322.218 598133.266 2321301.208 597864.381 | CaO: 53.6; MgO: 1.76 | 4.9 ha |
| Hai Duong | Hai Duong | Hai Duong | Hai Duong | Hai Duong | Hai Duong | Hai Duong | Hai Duong | Hai Duong |
| 1 | Van Chanh | Phu Thu Commune, Kinh Mon District | Phu Thu Commune, Kinh Mon District | Longitude: 106o32'47" Lattitude: 21o01'10" | Longitude: 106o32'47" Lattitude: 21o01'10" | Longitude: 106o32'47" Lattitude: 21o01'10" | CaO: 52.71-55.5; MgO: 0.19 -1.99 | C1+ C2: 2.036 |
| 2 | Hon Mountain | Phu Thu Commune, Kinh Mon District | Phu Thu Commune, Kinh Mon District | - | - | - | CaO: 54.05; MgO: 0.11 | P : 58.6 |
| 3 | Lu Chieu | Minh Tan Commune, Kinh Mon District | Minh Tan Commune, Kinh Mon District | Longitude: 106o34'45" Lattitude: 21o02'09" | Longitude: 106o34'45" Lattitude: 21o02'09" | Longitude: 106o34'45" Lattitude: 21o02'09" | CaO: 51.5-54.6; MgO: 0.45-3.14 | C1 : 138.72 |
| 4 | Trai Cach | Duy Tan Commune, Kinh Mon District | Duy Tan Commune, Kinh Mon District | Longitude: 106o30'45" Lattitude: 21o02'15" | Longitude: 106o30'45" Lattitude: 21o02'15" | Longitude: 106o30'45" Lattitude: 21o02'15" | CaO: 53-54; MgO: 0.25-1.0 | C2 : 30 |
| Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh | Ninh Binh |
| 1 | A number of quarries provided with conventional building materials by the People’s Committee of Ninh Binh Province | Dong Son, Quang Son and Gia Thanh communes, Gia Vien, Nho Quan districts, Tam Diep district-level towns, Hoa Lu and Kim Son districts | Dong Son, Quang Son and Gia Thanh communes, Gia Vien, Nho Quan districts, Tam Diep district-level towns, Hoa Lu and Kim Son districts | - | - | - | Quality for lime production ensured | Large deposits |
| Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh | Quang Ninh |
| 1 | Hoa Binh Stone Quarry | Thong Nhat Commune, Hoanh Bo District | Thong Nhat Commune, Hoanh Bo District | 2329410 36480606 2329420 36480380 2328970 36480430 2328920 36480270 2328960 36480040 | 2329410 36480606 2329420 36480380 2328970 36480430 2328920 36480270 2328960 36480040 | 2329410 36480606 2329420 36480380 2328970 36480430 2328920 36480270 2328960 36480040 |  | 16.8 ha |
| 2 | Bo Chuyen | Dai Yen Ward, Ha Long City | Dai Yen Ward, Ha Long City |  |  |  |  | 0.4 |
| 3 | Hong Thai Tay Stone Quarry | Hong Thai Commune, Dong Trieu District | Hong Thai Commune, Dong Trieu District |  |  |  |  | 2.19 |
| Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai | Lao Cai |
| 1 | Ma Tong | Pha Long Commune, Muong Khuong District | Pha Long Commune, Muong Khuong District | Longitude: 103o12'00" Lattitude: 22o45'00” | Longitude: 103o12'00" Lattitude: 22o45'00” | Longitude: 103o12'00" Lattitude: 22o45'00” |  | P: 500 |
| 2 | Van Ban | Khanh Yen Trung Commune, Van Ban District | Khanh Yen Trung Commune, Van Ban District | Longitude: Lattitude: | Longitude: Lattitude: | Longitude: Lattitude: |  | P: 10 |
| Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son | Lang Son |
| 1 | Co Stream | X. Hoa Lac Commune, Huu Lung District | X. Hoa Lac Commune, Huu Lung District | Longitude: 106o27'00 Lattitude: 21o33'00" | Longitude: 106o27'00 Lattitude: 21o33'00" | Longitude: 106o27'00 Lattitude: 21o33'00" | Cao: 55.7 ; MgO: 3.23 | P: > 100 |
| 2 | Dong Lai | X. Cai Kinh Commune, Huu Lung District | X. Cai Kinh Commune, Huu Lung District | Longitude: 106o22'25" Lattitude: 21o32'30" | Longitude: 106o22'25" Lattitude: 21o32'30" | Longitude: 106o22'25" Lattitude: 21o32'30" | CaO: 52 - 54; MgO: 1-1.5 | P: > 100 |
| 3 | Minh Tien | X. Minh Tien Commune, Huu Lung District | X. Minh Tien Commune, Huu Lung District | Longitude: 106o16'20" Lattitude: 21o33'20" | Longitude: 106o16'20" Lattitude: 21o33'20" | Longitude: 106o16'20" Lattitude: 21o33'20" | CaO: 50 - 53; MgO: 0.4-1.5 | P: > 1.440 |
| 4 | Quan Thanh | Xã Chi Lăng -H. Chi Lang Commune, Chi Lang District | Xã Chi Lăng -H. Chi Lang Commune, Chi Lang District | Longitude: 106o31'14"; Lattitude: 21o36'29" | Longitude: 106o31'14"; Lattitude: 21o36'29" | Longitude: 106o31'14"; Lattitude: 21o36'29" | CaO: 54.4; MgO: 04- 0.5 | P: 210 |
| Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen | Thai Nguyen |
| 1 | Truc Mai 1 | Lau Thuong Commune, Vo Nhai District | Lau Thuong Commune, Vo Nhai District |  |  |  |  | 50.68 ha 27.453 |
| 2 | Elephant Mountain | Chua Hang commune-level town, Dong Hy District | Chua Hang commune-level town, Dong Hy District |  |  |  | CaO: 54.7-55.5; MgO: 0.28 - 0.78 | 18.7 ha 3.804 |
| 3 | Lung Cho | Quang Son Commune, Dong Hy District | Quang Son Commune, Dong Hy District |  |  |  |  | 8.35 ha 9.53 |
| 4 | Xom Dau | Yen Lac Commune, Phu Luong District | Yen Lac Commune, Phu Luong District |  |  |  |  | 6.55 ha 5.4 |
| Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa | Thanh Hoa |
| 1 | Doc Ngan | Ngoc Khe Commune, Ngoc Lac District | Ngoc Khe Commune, Ngoc Lac District |  |  |  | CaO: 53.36; MgO: 1.01 | P: 224 |
| 2 | Cam Binh | Cam Binh Commune, Cam Thuy District | Cam Binh Commune, Cam Thuy District |  |  |  |  |  |
| Quang Binh | Quang Binh | Quang Binh | Quang Binh | Quang Binh | Quang Binh | Quang Binh | Quang Binh | Quang Binh |
| 1 | Ca Tang | Tam Hoa Commune, Tuyen Hoa District | Tam Hoa Commune, Tuyen Hoa District | VN-2000, Meridian 105, angle 6 degree | VN-2000, Meridian 105, angle 6 degree | VN-2000, Meridian 105, angle 6 degree | CaO: 58.45 – 55.49; MgO: 0.26 – 1.67 | P: 6.5 (141.0 (ha)) |
|  |  |  |  | X (m) | Y (m) | Y (m) |  |  |
|  |  |  |  | 1958.635 1959.501 1958.373 1957.958 | 603.860 604.573 605.751 604.646 | 603.860 604.573 605.751 604.646 |  |  |
| 2 | Trung Hoa | Trung Hoa Commune, Minh Hoa District | Trung Hoa Commune, Minh Hoa District | 1969.513 1969.161 1969.922 1969.000 | 603.825 604.477 605.097 604.408 | 603.825 604.477 605.097 604.408 | CaO: 53.27 – 54; MgO: 0.65 -1.29 | P: 175 (72.8.0 (ha)) |
| 3 | Quy Dat | Xã Quy - H. Quy Commune, Minh Hoa District | Xã Quy - H. Quy Commune, Minh Hoa District | 1984.125 1984.143 1982.852 1983.487 | 586.340 587.296 587.273 586.459 | 586.340 587.296 587.273 586.459 | CaO: 53.54; MgO: 1.26 | P : 350 (86.3 (ha)) |
| 4 | Minh Cam | Chau Hoa Commune, Tuyen Hoa District | Chau Hoa Commune, Tuyen Hoa District | 1969.057 1968.720 1968.534 1968.205 1967.842 1967.830 1968.027 1968.099 1968.224 1968.560 1968.567 1968.767 1968.954 | 626.463 627.056 627.783 628.006 627.921 627.605 627.558 627.272 627.114 627.081 627.772 627.742 627.399 | 626.463 627.056 627.783 628.006 627.921 627.605 627.558 627.272 627.114 627.081 627.772 627.742 627.399 | Quality for lime production ensured by Linh Thanh Company | 63.48 ha |
| Dak Lak | Dak Lak | Dak Lak | Dak Lak | Dak Lak | Dak Lak | Dak Lak | Dak Lak | Dak Lak |
| 1 | Dak Lak | Ban Dao Limestone Quarry, Ea Ie Commune, Ea Sup District (≥32 ha) | Ban Dao Limestone Quarry, Ea Ie Commune, Ea Sup District (≥32 ha) | 442141 442822 442944 442765 442040 | 1451096 1450775 1450279 1450231 1450982 | 1451096 1450775 1450279 1450231 1450982 | CaO: 54.47; MgO: 0.72; | 334b: 4.7 million m3 |
| Kien Giang | Kien Giang | Kien Giang | Kien Giang | Kien Giang | Kien Giang | Kien Giang | Kien Giang | Kien Giang |
| 1 | Ba He | X. Binh An Commune, Kien Luong District | X. Binh An Commune, Kien Luong District | Longitude: 104°36'05" Lattitude: 10°10'20" | Longitude: 104°36'05" Lattitude: 10°10'20" | Longitude: 104°36'05" Lattitude: 10°10'20" | CaO: 54.47; MgO: 0.72; | C1: 21 |
| 2 | Water Mountain | X. Binh An Commune, Kien Luong District | X. Binh An Commune, Kien Luong District |  |  |  |  |  |